## Slide 1: A Water-Flow Analogy for Teaching Data Reuse and Memory Hierarchies
Tanvi Sharma
Kaushik Roy
06/21/25

## Slide 2: Overview
Motivation
  Lowering the barrier to entry for AI hardware in one lecture for undergraduates
  Emphasis on the impact of data reuse on performance
Outline
  Examples of AI workloads
  A simple memory-compute model for AI hardware
  Introduction to water-flow analogy
  Memory- and compute- bound scenarios to understand data reuse
  Relation with roofline performance model
  Latency-bound scenario and implications
  Conclusion

## Slide 3: Artificial Intelligence (AI) Workloads
Artificial Intelligence (AI) is used everywhere in day-to-day applications such as chat-bots, text autocompletion, ad recommendations, summarization tasks and image recognition.
AI model architectures – Transformers (most common these days), CNNs, FFNs, RecSys, etc.
Transformer models
Convolutional Neural Networks (CNNs)
Recommendation Systems (RecSys)
(FFNs)
(FFNs)
Full Stack Optimization of Transformer Inference, 2023
ResNet Depiction
RecSys, Nvidia Blog

## Slide 4: Dominant Computation in AI workloads
Most AI workloads are dominated by GEMMs (GEneral Matrix Multiplications).
GEMMs are represented as GEMM(M, N, K).
AI hardware is designed to maximize performance of GEMMs.
Chart: 
| 128 | 256 | 512 | 1024
Matrix Multiplication | 91.2176 | 84.2315 | 72.0559 | 57.6846
Dropout | 3.1936 | 6.1876 | 9.98 | 14.5709
Softmax | 5.5888 | 9.98 | 17.5649 | 27.9441
RNN Runtime Distribution
Softermax. DAC 2021.
Approximate Computing AI Acceleration. IBM Blog 2018.
BERT-Large Latency % with sequence length
NonGEMMBench. ISPASS 2025
GEMM ()

## Slide 5: Common Examples of AI Hardware
Graphics Processing Units (GPUs) – started as domain specific ICs for accelerating graphics, now general-purpose programmable IC.
Tensor Processing Units (TPUs) – Domain specific IC specially designed for AI processing.
Neural Processing Units (NPUs) – Application Specific IC designed for one end system.
What do they have in common?

## Slide 6: Simple Memory-Compute Model for AI Hardware
Off-chip Memory
Compute
On-chip Memory
GEMM ()
x
=
Ki
Mi
Ni
Ki
Ni
Mi
A simple analytical model of AI hardware consists of
- off-chip memory (say DRAM or HBM)
- on-chip memory (SRAM)
- some compute units (ALUs or SIMD or Systolic Arrays)
Focus of this lecture - understand how data reuse in GEMMs impacts the hardware performance through a water-analogy.

## Slide 7: Waterflow-Analogy for Simple Memory-Compute Model
Off-chip Memory
Compute
On-chip Memory
GEMM ()
x
=
Ki
Mi
Ni
Ki
Ni
Mi
Tank – Off-chip memory
Tap – Memory Controller
Bucket – On-chip memory
Dishes – DNN operations, GEMMs
You – Compute
Water – Data (bytes)
Rate of doing dishes – Performance (operations/sec)

## Slide 8: Waterflow-Analogy for Simple Memory-Compute Model
Tank – Off-chip memory
Tap – Memory Controller
Bucket – On-chip memory
Dishes – DNN operations, GEMMs
You – Compute
Given the number of DNN operations and limited BW constraint, how to maximize Robs?

## Slide 9: Waterflow-Analogy Model Illustration (1) 9
Latency = 0.1 sec
Peak rate = 2 OPS
BW = 1L/sec
Assuming each dish requires 2L of water,
Peak rate (Rpeak) = 2 OPS * 2 L/op
= 4 L/sec
Case 1: Reuse factor (Freuse) = 1 OPs = 10 Data (required)
= 2 *10 / Freuse
= 20 L Tdata = L + Data/BW
= 0.1 + 20/1 = 20.1 sec
Tcomp = Data/Rpeak
= 20/4 = 5 sec Robs = 10/(20.1 + 0.5) OPS
= 0.485 OPS
time
Memory Controller
GEMMs
Compute
Say, Ops = 100.
How can we improve the performance? Does rate-matching memory bandwidth and compute throughput help?
2.1sec/OP
0.5 sec/OP

## Slide 10: Waterflow-Analogy Model Illustration (2) 9
Latency = 0.1 sec
Peak rate = 2 OPS
BW = 4 L/sec
Assuming each dish requires 2L of water,
Peak rate = 2 OPS * 2 L/op
= 4 L/sec
Water Analogy with caches/bucket
Case 2: Reuse factor (Freuse) = 1 OPs = 100 Data (effective) = 200 L
Data (required) = 2 *100 / Freuse
= 200 L Tdata = max(Ttap , Tbucket)
= max(200.1, 200/4) = 200.1 sec
Tcomp = Data/Rpeak
= 50 sec Robs = 100/200.6 OPS = 0.50 OPS
or dropping the tail latency,
Robs = 100/200.1 OPS = 0.50 OPS
Memory Controller
GEMMs
Compute
BW = 1 L/sec
On-chip SRAM
time
…
Caches are useful only if there are data reuse opportunities.

## Slide 11: Impact of Data Reuse on Performance (1) 9
Latency = 0.1 sec
Peak rate = 2 OPS
BW = 4 L/sec
Assuming each dish requires 2L of water,
Peak rate = 2 OPS * 2 L/op
= 4 L/sec
(a) Water Analogy with caches/bucket
Memory Controller
GEMMs
Compute
BW = 1 L/sec
On-chip SRAM
Case 3: Reuse factor (Freuse) = 2 OPs = 100
Data (effective) = 200L Data (required)
= 2 *100 / Freuse
= 100 L Tdata = max(Ttap , Tbucket)
= max(100.1, 200/4) = 100.1 sec
Tcomp = Data/Rpeak
= 200/4 = 50 sec (Ttap >> Tcomp) Robs = 100/100.1 OPS
= 0.99 OPS
time
Memory bound
…
Considering some dishes are not heavily soiled – can share same water for cleaning. 2L effectively acts as 4L for you.

## Slide 12: Impact of Data Reuse on Performance (2) 9
Latency = 0.1 sec
Peak rate = 2 OPS
BW = 4 L/sec
Assuming each dish requires 2L of water,
Peak rate = 2 OPS * 2 L/op
= 4 L/sec
(a) Water Analogy with caches/bucket
Memory Controller
GEMMs
Compute
BW = 1 L/sec
On-chip SRAM
Case 3: Reuse factor (Freuse) = 4 OPs = 100
Data (effective) = 200L Data (required)
= 2 *100 / Freuse
= 50 L Tdata = max(Ttap , Tbucket)
= max(50.1, 200/4) = 50.1 sec
Tcomp = Data/Rpeak
= 200/4 = 50 sec (Ttap ~ Tcomp) Robs = 100/50.1 OPS ~ 2 OPS (Rpeak)
Considering dishes are soiled only slightly – more dishes can share same water for cleaning. 2L effectively acts as 8L for you.
time
…
Balanced

## Slide 13: Impact of Data Reuse on Performance (3) 9
Latency = 0.1 sec
Peak rate = 2 OPS
BW = 4 L/sec
Assuming each dish requires 2L of water,
Peak rate = 2 OPS * 2 L/op
= 4 L/sec
(a) Water Analogy with caches/bucket
Memory Controller
GEMMs
Compute
BW = 1 L/sec
On-chip SRAM
Case 3: Reuse factor (Freuse) = 8 OPs = 100
Data (effective) = 200L Data (required)
= 2 *100 / Freuse
= 25 L Tdata = max(Ttap , Tbucket)
= max(25.1, 200/4) = 50 sec
Tcomp = Data/Rpeak
= 200/4 = 50 sec (Ttap < Tcomp) Robs = 100/50 OPS = 2 OPS (Rpeak)
Say some notorious kid have put already clean dishes in the sink – more water reuse. 2L effectively acts as 16L for you.
Compute bound
time
…
…

## Slide 14: Roofline: Memory vs Compute intensive
A workload is considered memory intensive if
Time to fetch data > Time to perform computations
Data Reuse affects the nature of workload
Operations/Byte (Arithmetic Intensity)
Low reuse -> memory bound region
  Performance limited by memory bandwidth
High reuse -> compute bound region
  Performance limited by peak throughput
Memory bound
Data Reuse (Ops/B)
Compute bound
Observed Throughput
(OPS)
Peak Throughput (OPS)
Roofline Performance Model
Bandwidth (B/s)
Notes: Now if we try to plot data reuse along the x axis

## Slide 15: Arithmetic Intensity of GEMMs (1)
Theoretical (or algorithmic) AI for GEMMs =
Will the following GEMMs be in compute bound or memory bound region?
    For a GPU with 130 TFLOPS peak throughput and 1000 GB/s DRAM bandwidth
  GEMM (1024, 1024, 1024)?
    = 2M/3
C
K
M
x
K
M
=
B
A
N
N
…
…
…

## Slide 16: Arithmetic Intensity of GEMMs (2)
Theoretical (or algorithmic) AI for GEMMs =
Will the following GEMMs be in compute bound or memory bound region?
    For a GPU with 130 TFLOPS peak throughput and 1000 GB/s DRAM bandwidth
  GEMM (1024, 1024, 1024)
  GEMM (4, 1024, 1024)?
    =~ 2M
C
K
M
x
K
M
=
B
A
N
N
…
…
…

## Slide 17: Roofline: Memory vs Compute intensive
A workload is considered memory intensive if
Time to fetch data > Time to perform computations
Factors affecting workload nature:
Data Reuse or Arithmetic Intensity (AI)
  Water shared by multiple dishes/how much they are soiled (GEMM shape)
Hardware Specifications
  physical limitations on how many dishes can be washed per second (peak throughput)
  Limited tap water bandwidth (main memory bandwidth)
Memory bound
AI or Data Reuse (Ops/L)
Compute bound
Observed Throughput
(OPS)
Ridge Point AI = 2
AI or Data reuse = (1 Op/2 L)*Freuse
Ridge Point AI = 2 OPS/1 L/s = 2 Ridge Point Freuse = 2/(1/2) = 4
Is it always necessary for a workload to be either in the memory bandwidth- or compute- bound region?
Peak = 2 OPS
1 L/s
Notes: Now if we try to plot data reuse along the x axis

## Slide 18: Examples of Memory-bound Scenarios
Latency = 1 sec
Peak rate = 200 OPS
BW = 400 L/sec
Assuming each dish requires 2L of water,
Peak rate = 200 OPS * 2 L/op
= 400 L/sec
Memory Controller
GEMMs
Compute
BW = 10 L/sec
On-chip SRAM
(a) Memory-bandwidth bound
Case 6: Reuse factor (Freuse) = 1 OPs = 1000
Data (effective) = 2000 L Data (required)
= 2 *1000 / Freuse
= 2000 L Tdata = max(Ttap , Tbucket)
= max(1+2000/10, 2000/400) = 201 sec
Tcomp = Data/Rpeak
= 2000/400
= 5 sec
(Tdata >> Tcomp) Robs = 1000/201 OPS
= 4.98 OPS << 200 OPS
(b) Memory-Latency bound
Case 7: Reuse factor (Freuse) = 4 OPs = 4
Data (effective) = 8 L Data (required)
= 2 *4 / Freuse
= 2 L Tdata = max(Ttap , Tbucket)
= max(1+2/10, 8/400) = 1.2 sec
Tcomp = Data/Rpeak
= 8/400
= 0.02 sec
(Tdata >> Tcomp) Robs = 4/1.2 OPS
= 3.33 OPS << 200 OPS

## Slide 19: Conclusion
Proposed a simple waterflow-analogy for showcasing the impact of data reuse on AI hardware performance.
Connected the concepts to the roofline performance model with worked-out examples.
Used in the first offering of AI Hardware course at Purdue – where students were from different backgrounds (from pure algorithm to circuit designers).
The given slides can be used prior to introducing dataflow or scheduling strategies, lowering the barrier to AI hardware concepts.

## Slide 20: Q&A
Thank you. Any feedback?

## Slide 21: Appendix

## Slide 22: Recap: Evaluating DNNs
Simple memory-compute model
Arithmetic Intensity (data reuse)
Roofline performance model
  Memory bound region
  Compute bound region
Off-chip Memory
Compute
On-chip Memory
Question:
For a GPU with 130 TFLOPS peak throughput and 1000 GB/s DRAM bandwidth, what will be the minimum value of arithmetic intensity for it to be compute bound?
(transition AI)

## Slide 23: Recap: Roofline Performance Model
GFLOPS = GFLOP/s
  Giga Flop Operations per second
  Throughput
Arithmetic Intensity (AI) = Reuse
  FLOPs/Byte
Transition @ AI
  Time to fetch data = Time to compute
Transition @ AI = Peak GFLOPs/Peak GB/s
Notes: now as Adi asked in the last class, what does this throughput and data reuse mean in terms of neural networks?

## Slide 24: Recap: Matrix Multiplications in DNN Models (1)
For a layer in MLP with
  Input dimension – din
  Output dimension – dout
  Pytorch: nn.Linear
x
din
dout
dout
=
N
(matmul)
din
N
N
N
Weights
Activation
Output
Notes: remember that neural networks can be thought of as matrix multiplications for MLPs

## Slide 25: Recap: Matrix Multiplications in DNN Models (2)
For a convolution layer with
  Filter size – R x S x C
  Input fmap size – H x W x C
  Output fmap size – P x Q x K
  Batch size – N
  Implicit GEMM algorithm using im2col transformation
    (GEMM – general matrix multiplication)
RSC
NPQ
x
K
RSC
NPQ
=
K
Weights
Activation
Output
Notes: CNNs

## Slide 26: Recap: Matrix Multiplications in DNN Models (3)
For an attention layer with
  sequence length – n
  embedding dimension – dk (=v=q)
  heads = h
  Static matrix multiplications – Q, K, V, Output
  Dynamic matrix multiplications – QKT, QKTV
  e.g.
dk/h
n
x
n
dk /h
n
=
n
KT
Q
QKT
Notes: even in attention layers

## Slide 27: Basic Computations in AI Workloads
Dot Product (a . b = aTb = c)
  Product is a scalar value
  Vectors typically treated as column vectors
  Used to measure similarity, also referred as inner product
.
a
b
a1
a2
.
.
.
.
an
b1
b2
.
.
.
.
bn
=
a1 | a2 |  |  |  |  | an
x
b1
b2
.
.
.
.
bn
c
MAC (multiply and accumulate)
Number of operations?

## Slide 28
Matrix Vector Multiplication (ATb = c)
  Product is a vector
  Each element in output vector is dot product of row of AT and the vector b
a11 | a12 | . | a1m
a21 | a22 | . | .
. | . | . | .
. |  | . | .
. |  |  | 
. |  |  | 
an1 | an2 | . | anm
b1
b2
.
.
.
.
bn
Basic Computations in AI Workloads
Notes: Each output is a dot product between the row of input matrix and the other vector

## Slide 29: Basic Computations in AI Workloads
Matrix Vector Multiplication (ATb = c)
  Product is a vector
  Each element in output vector is dot product of row of A and the vector b
a11 | a21 | . | . | . | . | an1
a12 | a22 | . | . | . | . | an2
. | . | . | . | . | . | .
a1m | a2m | . | . | . | . | anm
x
b1
b2
.
.
.
.
bn
=
c1
c2
.
.
cm
Notes: Each output is a dot product between the row of input matrix and the other vector